## Slide 1: Modern Dataflow in Experimental Nuclear Science (and Tcl).
Ron Fox, Giordano Cerizza Sean Liddick, Aaron Chester

## Slide 2: Talk Outline
A bit about me and my Tcl history
What is the National Superconducting Cyclotron Laboratory (NSCL)
How data taking has evolved in experimental nuclear science
E17011 an experiment with modern electronics – why it’s computationally demanding
Parallel resources available to us
Message Passing Interface (MPI) and Tcl
  Intro to MPI
  Existing Tcl support
  Tcl-Ish support we did.
Applying MPITcl to an existing application
What this means for experimental nuclear science at the NSCL

## Slide 3: Tcl and me.
Introduced Tcl/Tk at the National Superconducting Cyclotron Lab (NSCL) back in the 4.x days.
Plugged into the community with a talk in New Orleans (Tcl 2004)
  https://www.tcl.tk/community/tcl2004/Papers/RonFox/
  NSCLSpecTcl – Histogramming package for experimental nuclear science.
Tcl/Tk conference proceedings editor from Tcl2005 and on if memory serves.
Tcl plays an important role in the NSCL experimental program.

## Slide 4: The National Superconducting Cyclotron Lab.
Located at Michigan State University
Funded by the National Science Foundation as a user facility
Explore the properties of nuclear unstable nucleii
Why and how do certain isotopes form.
Where do the heavy elements come from?
http://www.nscl.msu.edu

## Slide 5: NSCL Block Diagram

## Slide 6: Science drivers for Rare Isotope Research

## Slide 7: Data Acquisition – old school (analog)
Detector
Preamp.
Shaping Amp
Discrimination
Logic and timing
ADC, TDC, QDC
Important point – dead-times for a conversion are microseconds

## Slide 8: Data Acquisition – old school (analog)
Detector signals
Pre-amplification
Shaping/amplification
Timing/triggering
Digitizing modules
Each digitizing module Gives one value per input:
Pulse height
Pulse charge integration
Pulse timing relative to some reference time.

## Slide 9: Modern Data Acquisition (digital)
Detector
Preamp.
Flash ADC (100-500MHz)
Large FPGA
Memory

## Slide 10: Modern data acquisition (100MHz – 500MHz)
Detector Signals
Preamplification
Digitization
Firmware can extract
  Pulse ht.
  Charge integral
  Timing
Keeping waveforms allows experiments that can’t be done with analog electronics.
Wave form analysis is computationally demanding Wave forms bloat the data

## Slide 11: E17011
Scheduled to run in January.
  Look at beta decay of 80Ga -> 80Ge
  Look at the lifetime of the 02+ -> 01+
  Lifetime tell us something about the difference in the radius of the charge distribution of the two states.
200MB/second sustained – though modest trigger rate (~3KHz).
Will take 100TB+ of data
Need good online and nearline analysis:
  Are the detectors working.
  Are we seeing what we think we should be seeing.
  Should we ask for additional (discretionary time).

## Slide 12: E17011 – block diagram
Ron Fox Tcl 2019, Houston, TX
, Slide 12
Sketch of experiment
86Kr primary beam 104MeV/A
9Be
Production target
80Ga 80Ga β- decays to 80Ge
Si
PIN stack
Beam particle ID
CeBr3
Pixilated PMT
LaBr3
LaBr3
LaBr3
Ge
Ge
Ge

## Slide 13: Pictures pictures (CeBr3 and LaBr3 array)

## Slide 14: More pictures Ge Array (SeGA)

## Slide 15: What happens to the implanted ions.
80Ga decays to 80Ge by β- decay.
  This decay is also detected in the CeBr3 detector
  This decay populates several energy levels of 80Ge
Of interest are the decays that populate the 02+ state.
  This eventually de-excites to the 01+ state emitting a γ-ray (detected by the LaBr3 array and/or SeGA) and and a conversion electron.
  The conversion electron produced by that decay is sensed by the CeBr3
Well it’s not actually eventually.
  Similar de-excitations have half lives of about 50ns.
  We want the actual ½ life.
This is a short ½ life. How to measure it.
  Digitize the pulses in the CeBr3
    Sum signal at 500MHz
    pixels at 250MHz
    Trace lengths of a few microseconds (on order 100 samples).

## Slide 16: Sample trace from a similar experiment
Decay time
Conversion e- energy

## Slide 17: Where does that 200MB/sec come from?
Since most of the CeBr3 detector lights up for a hit we about 200traces/event (maximal pixel is ‘where’ the event occurred).
The data rate is dominated by traces from the CeBr3.
Trigger rates may be 3KHz (modest)
Data transfer rates will be a sustained 200MB/seconds.
To see if the experiment is “working” we need to do some processing on all this stuff.
  Determine if traces are single or double pulses.
  Determine the characteristics of the pulse(s) – time and height.
Good news though: Taking traces meas we can do the experiment.
This experiment is really hard to do with old school electronics.

## Slide 18: Data Flow:
XIA digitizers Crate 1
XIA
Digitizers
Crate 2
Data emitted
Have 50Mhz timestamps
Synchronized to < 1ns.
Event builder
Event Selection
(PIN Based)
Append Fits for 1,
2 pulses to
Sum signal.
Online storage
100TB
130 TB Cephs
Analysis Storage
Periodic
rsync
Near-line analysis
Threaded
NSCLSpecTcl
(see later)

## Slide 19: Online analysis
Fit the sum traces from the CeBr3.
  Fit for both single and double pulses.
  Use a heuristic to determine if the pulses are single or double.
Make a pile of histograms (NSCLSpecTcl) and look at them online
Keep up with the incoming data rate.
NOTE: Each fit costs 3.5ms to do using GSL’s Levenberg-Marquardt.
Serial code isn’t going to cut it.

## Slide 20: Near-line Analysis – want to keep up with incoming data rate or better
Fit the remaining traces in the CeBr3
  Are they single or double pulses (heuristic)?
  If double pulses extract the time difference as a parameter for histogramming.
Correlate implantation events with decay events.
  Using position and particle ID information
  Timing between implantation and decay.
These are computationally intensive (e.g. the fit is about 3.5ms/event). To make decisions about the experiment we need to analyze the data already taken faster than acquisition.
Serial code isn’t going to cut it ~2500 cores just for fitting all traces.

## Slide 21: Parallel resources at the NSCL available to E17011
Three high core count systems:
  1 26 core system. (Xeon E5-2690 v4 @ 2.60GHz)
  2 40 core systems (Xeon Gold 6148 @ 2.4GHz) – bought for this experiment
  Used for online data flow and interactive ‘near-line’ analysis.
Modest Linux cluster
  360 cores of various ages
  Used for non-interactive ‘near-line’ partial analysis.
That’s not going to be enough (to do the fitting of all signals at data rates needs about 2500cores).
no GPU coprocessors 

## Slide 22: MSU Institute for Cyber Enabled Research (ICER)
Cores 23,126
Storage
7 PB
Naturally we’ve lusted after sought ways to leverage this resource for near-line and maybe even online analysis.
Work to containerize our apps is done (thank you singularity)
Scheduling, however can be an issue: NSCL resources can be dedicated to E17011, ICER is shared across all university users.

## Slide 23: Structure of event analysis parallel programs
src
Data distribution
worker
worker
.
.
.
Sort
output
Sink

## Slide 24: Meeting these needs.
Different types of parallelism
  Threaded parallelism for the online/interactive stuff.
  Distributed parallelism for near-line non-interactive stuff.
Tools to make parallelization simpler
Fitting:
  Support for GPU ‘accelerated’ fitting residual and Jacobian computation 
  Machine learning for single/double pulse determination – most traces are single pulses
Example trace fitting the sum signal: same program threaded/cluster
Chart: Event/sec vs processors
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
Fireside | 281.0663 | 552.5476 | 1065.5513 | 1960.4626 | 4173.4091 | 6189.7753 | 8607.6562 | 15302.5 | 21188.0769
HPCC scratch->scratch clump 1000 | 185.0487 | 668.5558 | 856.7496 | 2586.338 | 4552.8099 | 8607.6562 | 17215.3125 | 21188.0769 | 27544.5
Chart: Events/sec vs workers
| 1 | 2 | 4 | 8 | 16 | 32 | 40 | 41 | 42 | 44 | 48 | 56 | 72 | 80
 | 263.1579 | 526.3158 | 1063.8298 | 2127.6596 | 4166.6667 | 7692.3077 | 9090.9091 | 10000 | 10000 | 10020.0401 | 10593.2203 | 10799.1361 | 11235.9551 | 11764.7059

## Slide 25: MPI – cluster distributed parallel computing
MPI - Message Passing Interface standard for writing distributed parallel programs.
  OpenMPI https://www.open-mpi.org/
  MPICH https://www.mpich.org/
Multiple instances of the same process run in parallel.
  Each process as a rank identifying it.
  Processes can target messages to specific ranks.
  Communicators can be formed to link groups of processes together.
Messages require:
  Rank – who we’re sending to but:
  Communicator – defines the process group in which the rank has meaning (MPI_COMM_WORLD – the entire application is pre-defined).
  A Tag (integer)
  Message data.
  Type of data in the message (message data are strongly typed)
  Number of items of that type being sent.

## Slide 26: The MPI API is large and complex:
… and there’s more…much more.

## Slide 27: Approaches for encapsulating MPI Subset wrapping
Straight encapsulation of the MPI function interface.
  Approach taken by Axel Kohlmeyer for the mpi package
  See e.g. https://core.tcl-lang.org/jenglish/gutter/packages/mpi.html
Still captures the flavor of the MPI API
Still exposes explicitly the MPI API subset
Still exposes the complexity.

## Slide 28: What do Tcl MPI applications want to do:
Send scripts executed in other ranks.
  Special case of send to all or all others.
Send data that can be handled by other ranks via callbacks.
  Again special case of send to all or to others.
Tcl – We know in advance: Everything has a string representation.
Binary data – may be sent around by the C/C++ part of the application for C/C++ parts of the application to work on needs a way for that code to shove the TclMPI event handling stuff aside and take over.

## Slide 29: mpitcl - MPI aware tcl shell.
Provides MPI aware tclsh.
  Must be run from mpirun.
All ranks run this.
Rank 0 is special – the ‘master’ interpreter it takes input from stdin (normally a file for cluster batch jobs).
Provides all processes with the mpi namespace in which the mpi command ensemble lives.
Rank 0 runs a thread to hoist MPI messages received to the event loop (vwait).
Ranks other than zero run a main loop that accepts MPI messages and act on them under the assumption they come from mpitcl.
MPI Tags are used to transparently dispatch messages to appropriate handlers.

## Slide 30: mpi::mpi command ensemble subcommands:
size - How many processes are in the application.
rank – What is my rank in MPI_COMM_WORLD
execute where script – Executes a script in the rank(s) defined by where where is
a rank number “all” or “others”
send where data - sends the data to where
handle script - specifies script to handle data received. The script
receives two parameters: sender rank and the data.
stopnotifier - only legal in rank 0 – stops the event notifier thread.
startnotifier - only legal in rank 0 – starts the notifier thread again.

## Slide 31: Sample mpitcl scripts:
mpi::mpi stop notifier
mpi::mpi send all exit
Mimimal MPI
script
proc receiver {rank data} {
puts "Received from $rank '$data'"
incr ::slaves -1
}
set slaves [mpi::mpi size]
incr slaves -1; # number of slave processes.
mpi::mpi handle receiver
mpi::mpi execute others {
mpi::mpi send 0 "Rank [mpi::mpi rank] is alive"
}
while {$slaves} {
vwait slaves
}
mpi::mpi stopnotifier
mpi::mpi execute all exit
Soliciting/getting data from workers

## Slide 32: Applying tclmpi – The Circle is complete.
NSCLSpectcl
Structure
Parallelization of the interactive version (threaded).
Creating a batch NSCLSpecTcl and using it with tclmpi.

## Slide 33: NSCLSpecTcl is highly interactive

## Slide 34: Simplified NSCLSpecTcl structure and parallelization approaches.
Extended Tcl/Tk Interpreter
Data Source
(File or pipe)
High level Buffer Decoding
User Event
Processing
pipeline
Gating and
Histogramming
Blocks of data
Raw events
Raw and synthetic parameters
Analysis config.
Creates
Configures
And controls

## Slide 35: Threaded Parallelism (Giordano Cerizza)
Extended Tcl/Tk Interpreter
Data Source
(File or pipe)
Gating and
Histogramming
Blocks of data
High level Buffer Decoding
User Event
Processing
pipeline
Raw events
Decoded and synthetic parameters
Analysis config.
Creates
Configures
And starts
High level Buffer Decoding
User Event
Processing
pipeline
…
User code must be thread-safe

## Slide 36: Threaded Spectcl performance
Chart: Number of Processors
| 2 | 4 | 8 | 16 | 24 | 32 | 40
INPROC | 425 | 706 | 1410 | 2416 | 2749 | 3042 | 3062
Roll off is at the performance limit of the SSD that contained the data.
Analysis pipeline for this case is simple compared with E17011’s.
Good scaling up until SSD transfer limits.

## Slide 37: MPI parallelism?
We can recruit more cores if the application scales.
We don’t have to worry about thread safety since it’s process parallelism.
With an assist from container technology (e.g. singularity) we can get outside the NSCL to supercomputer centers (or ICER e.g.) with even more cores.
BUT In almost all cases cluster computing doesn’t allow dynamic interactivity.
  Needed to turn NSCLSpecTcl into a batch program.
  Needed to figure out how to easily parallelize it.
  This is the original target of mpitcl.

## Slide 38: MPI NSCLSpecTcl
Each process is a complete batch NSCLSpecTcl
  Batch NSCLSpecTcl is three packages
    spectcl – the base application code.
    mpispectcl MPI data sources and sinks.
    A user supplied package implementing the processing pipeline.
  Batch/MPI NSCLSpecTcl has generalized data sources and sinks. analyze command sends blocks of events from source to sink. I’ve implemented:
    Source –file.
    Source – MPI (for workers – requests block of data from rank 0).
    Sink -- Analysis
    Sink – MPI (Distributes blocks of data to workers using MPI source).
Rank 0 :
  Tells each process (including itself) to read in the configuration scripts.
  Tells other process to use an MPI Source and Analysis sink
  Tells itself to use a file data source and MPI sink.
  Tells everyone to start analyzing data.
When analysis is complete Rank 0
  Tells all other processes to send it spectrum data.
  Sums the spectra into total spectra
  Writes them out for visualization.

## Slide 39: What this looks like:
mpi::mpi execute all {
package require spectcl
package require mpispectcl
package require MyPipeline; # User event processing code is here.
source defs.tcl
}
mpi::mpi execute others {
mpisource
analysissink
}
filesource run-0003-00.evt
mpisink
mpi::mpi stopnotifier
mpi::mpi execute others analyze
analyze
mpi::mpi startnotifier

## Slide 40: Getting the data back:
set l [spectrum -list]
set f [open spectra.dat w]
foreach spectrum $l {
set name [lindex $spectrum 1]
getSpectrumFromWorkers $name
swrite -format ascii $f $name; # Writes a histo to file.
}
close $f

## Slide 41: Summing a spectrum from worker nodes.
proc addData {name src data} {; # sums the histo from 1 worker into the local histo.
foreach datum $data {
set value [lindex $datum end]
set coords [lrange $datum 0 end-1]
set current [channel -get $name $coords]
incr current $value
channel -set $name $coords $current
}
incr ::expected -1
}
proc getSpectrumFromWorkers name {
mpi::mpi handle [list addData $name]
set ::expected [mpi::mpi size]
incr ::expected -1;
set script "mpi::mpi send 0; # Care must be taken to ensure substitutions are done
append script "\[“ ; # in the right process.
append script "scontents $name]"
mpi::mpi execute others $script
while {$::expected > 0} {
vwait ::expected;
}
}

## Slide 42: Does this work?
10Gbyte file with 2,754,450 events. |  |  |  |  | 
Workers | Time | MB/sec | Events/sec |  | 
1 | 25.4 | 403.1496 | 108442.91 |  | 
2 | 13.5 | 758.5185 | 204033.33 |  | 
4 | 6.6 | 1551.515 | 417340.91 |  | 
8 | 3.9 | 2625.641 | 706269.23 |  | 
Chart: Events/sec
| 1 | 2 | 4 | 8
 | 108442.9134 | 204033.3333 | 417340.9091 | 706269.2308
2.6Gbytes/sec is interconnect saturation (dual 10GBit/sec ethernet)
Event processing in the actual experiment will be more complex but we can scale to more workers.

## Slide 43: Conclusions
NSCL’s Transition to modern, digital nuclear electronics poses problems for online and near-line data analysis.
Experiments will increasingly require parallelism in online and near-line data handling:
  Software tools to make it easy for naïve users to make use of parallelism by plugging in their event analysis code.
  Large core count systems for interactive, online analysis (threaded parallel).
  Clusters dedicated to the running experiment for near-line analysis (distributed parallel).
  High speed interconnects to support the data flow bandwidth.
  Large, multi-petabyte storage that’s fast with fast interconnects.
E17011 provides a laboratory to explore the techniques we’ll need to apply to modern experiments.
mpitcl is one technique to simplify parallel programming for “the masses”
  Easly retrofitted a highly interactive, complex serial analysis program (2 days work)
  Got scaling up to the interconnect bandwidth.